## Slide 1
The Genome Assembly Workshop
Lutz Froenicke
DNA Technologies & Expression Analysis Cores
UC Davis Genome Center
2020
Human Chromosomes. Credit: Jane Ades, NHGRI

## Slide 2: DNA Technologies & Expression Analysis Cores
HT Sequencing Illumina
Long-Read & Linked Read Sequencing PacBio, Oxoford Nanopore, 10X Genomics
HMW DNA isolation
Illumina microarray (genotyping)
Consultations  Experimental Design (Bioinformatics Core & DNA Tech Core)
introducing new technologies to the campus
shared equipment
teaching (workshops)

## Slide 3: The DNA Tech Core Team
Emily
Oanh
Siranoosh
Vanessa
Diana
Ruta

## Slide 4
MacLellan, W. R. et al. (2012) Systems-based approaches to cardiovascular disease
Nat. Rev. Cardiol. doi:10.1038/nrcardio.2011.208
The UCD GENOME CENTER
DNA Tech & Expression Analysis
Proteomics Core
Metabolomics Core
“DNA makes RNA and RNA makes protein“
the Central Dogma of Molecular Biology; simplified from Francis Crick 1958

## Slide 6: DNA Tech Genome Assembly Tools
10X Genomics Chromium Genome “linked-reads”
PacBio Sequel II “super-long reads” >20kb
PacBio Sequel “high-fidelity-long reads” (Q20,Q30, 15kb & 20kb)
PromethION Nanopore “super-long reads” >20kb
MinION Nanopore “ultra-long reads” >100 kb
Bionano Optical Genome Mapping (scaffolding) > 150 kb
Hi-C (chromosome scale genome scaffolding)

## Slide 7: Bionano Saphyr Optical Genome Mapping

## Slide 9: Experience 200+ species/varieties with PacBio 140+ species with 10x Genomics as of December 2019

## Slide 10: DNA Quality !!!
HMW DNA isolation
  Physical damage (PFGE image is not fully informative)
  Chemical damage
  Chemical contamination
  Sample specific protocols?
  Nuclei isolation, agarose plugs
  Cell culture?
  Rescue efforts (BluePippin; DNA damage repair) tend to have minimal impact

## Slide 11: Input DNA requirements for gDNA sequencing
Good quality, high molecular weigh DNA >50Kb in length
Free of contaminants such as polysaccharides, proteins, salts, etc
Nanodrop ratio of 260/280=1.8 260/230=2.0

## Slide 12
DNA isolation protocol
Liquid nitrogen grinding + sorbitol pre-wash + CTAB buffer lysis + Sodium acetate and isopropanol precipitation ( Inglis et al)
Pippin pulse gel image
Femto trace

## Slide 13
ONT library prep protocol: 50Kb shear + SRE, LSK109 library prep
Name | Total yield | Read length N50 | Bases >100Kb and Q7 (% of total data) | Bases >200Kb and Q7 (% of total data)
Ninja | 81Gb | 36Kb | 0.4Gb (0.4%) | 0.6Mb(0.0007%)
US96UC23 | 52Gb | 36Kb | 0.3Gb (0.6%) | 0.6Mb(0.001%)
Pi251246 | 94Gb | 37Kb | 0.6Gb (0.6%) | 4.6Mb (0.04%)
Ar Seriola | 98Gb | 37Kb | 0.8Gb (0.8%) | 7.1Mb(0.007%)
Salinas | 93Gb | 27Kb | 0.1Gb (0.19%) | 0.4Mb (0.0004%)
PromethION run results
Longest read ~200Kb range

## Slide 14: Complementary Approaches
Illumina | PacBio CLR | PacBio HiFi | PromethION Nanopore
Still-imaging of clusters (~1000 clonal molecules) | Video recordings fluorescence of single molecules | Video recordings fluorescence of single molecules | Recording of electric current through pores
Short reads - 2x300 bp Miseq | Up to 70 kb, N50 25 kb | Up to 20 kb, N50 18 | Up to 100 kb, N50 30 kb
Repeats are mostly not analyzable | spans retro elements | accurate enough to assemble through REs | spans retro elements
High output - up to 2.4 Tb per lane | up to 100 Gb per SMRT-cell | up to 25 Gb HiFi data per cell | Up to 100 Gb per flowcell
High accuracy ( < 0.5 %) | Raw data error rate 15 % | CCS data < 0.1% | Raw data error rate 8 %
Considerable base composition bias | No base composition bias | No base composition bias, but still mononucleotide repeat problem | Some systematic errors,
Very affordable | Costs 3 to 5 times higher | Costs 3 to 5 times higher | Costs 2x higher
De novo assemblies of thousands of scaffolds | “Near perfect” genome assemblies | “Near perfect” genome assemblies; lowest error rate | “Near perfect” genome assemblies with suppl. data; highest contiguity

## Slide 15: Strengths and weaknesses (diploid genomes)
 | 10X/TELL-Seq | Sequel CLR | Sequel HiFi | PromethION
Accuracy –single read | 4 | 1 | 4 | 2
Accuracy - consensus | 4 | 4 | 4 | 3
Contiguity | 1-2 ? | 3-4 | 3 | 4
Yield/$ | 4 | 4 | 2 | 4
In many case the resulting assembly quality will depend on the DNA sample quality as well genome organization (repeat content/length).
Pacbio relative even performance ( fish ?; jellyfish?)
Nanopore: significant variance between organisms Plants ++; birds -, fish -, jellyfish -

## Slide 16
How does nanopore sequencing work ?
Raw data fast5
fastq
ATCG
Basecaller
RNN, flip-flop
Guppy 3.2.8
Huge data size

## Slide 17
non-random errors

## Slide 18
70 nm aperture
“Zero Mode Waveguide”

## Slide 19: SMRT-bell adapters circular sequencing
Source: PacBio

## Slide 22: Iso-Seq Pacbio
Sequence full length transcripts  no assembly; default for gene annotation
High accuracy
More than 95% of genes show alternate splicing
On average more than 5 isoforms/gene
Precise delineation of transcript isoforms (PCR artifacts? chimeras?)

## Slide 23
Source: PacBio

## Slide 24
Source: PacBio

## Slide 25
Source: PacBio

## Slide 27: Coffee 2017: arabica 1.3 Gb genome Medrano et al. PacBio & ChICAGO scaffolding Scaffold N50 = 2.24 Mb Contig N50= 1.31 Mb 2015: robusta 0.7 Gb

## Slide 28: PromethION read lengths
RL histogram arabica

## Slide 29: Yield over time

## Slide 30: Bionano Optical Genome Mapping
Contig N50 of assembly > 40 kb
In silico digests

## Slide 31: Hi-C chromosome-scale scaffolding

## Slide 32
Future’s so bright

## Slide 33: Thank you!
Let’s get started!

## Slide 34
The Blue Pippin Prep System
Automated Preparative Gel Electrophoresis for NGS
Instrument contains:
Electrophoresis pulsed-field gel electrophoresis power supply
Electrode array
Fluorescence detection optics
Single-board PC with control software

## Slide 35
The BluePippin Prep System
Automated Preparative Gel Electrophoresis for NGS
Confidential, Sage Science
35