## Slide 1: Single Cell Sample Preparation
Diana Burkart-Waco, PhD
dburkart@ucdavis.edu
SRA at UC Davis DNATECH Core
https://dnatech.genomecenter.ucdavis.edu/

## Slide 2: Overview
Why single cell?
Methods – SC isolation
  Single cell isolation
  Single nuclei
Methods - sample QC
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
Cell labeling
Single cell studies at DNA Tech

## Slide 3: scRNA-seq

## Slide 4
Captures 100-10,000+ cells per sample.
Recovers up to ~65% of cells.
Low doublet rate.
  (~0.9% per 1,000 cells).
40 micron size limit.
Expensive!
10X Genomics

## Slide 5
Homemade drop-seq.
Qiagen UPX.
BD Rhapsody.
SPLIT-seq.
Dolomite Nadia System.
Fluidigm.
And the list goes on…
Alternative technologies
Need both single cells and to maintain sample composition.

## Slide 6
Use combinatorial barcoding to label cells of origin.
Great because don’t need fancy equipment.
Increased cell size limits.
Input = fixed cells or nuclei.
https://www.splitbiosciences.com/
SPLIT-Seq
Blattman et al. 2020. Nature Microbiology

## Slide 7: BD Rhapsody
Inject cells into cartridge and fall into microwells with barcoded beads.
Similar cell size limit and cost to 10X.
Higher capture rate.
More flexibility in targeted capture with custom beads.

## Slide 8: Overview
Why single cell?
Methods – SC isolation
  Single cell isolation
  Single nuclei
Methods - sample QC
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
Cell labeling
Single cell studies at DNA Tech

## Slide 9: Cell isolation
Cell isolation guides available at:
https://www.support.10xgenomics.com/single-cell-gene-expression/sample-prep/
Cell isolation  biggest source technical variation.
Dissociation and preparation depends on cell type.

## Slide 10: General Workflow
Tissue dissection
Mechanical mincing
Enzymatic breakdown
Cell enrichment
(optional)
Obtain cell interest (flow)
Remove dead cells (beads, etc.)
E.g. Trypsin, dispase, collagenase)
Often with agitation
Trituration, razor blade, etc.
Fast, reliable, clean.

## Slide 11: Tissue Dissociation
Many ways to dissociate tissue:
  Mechanical
  Enzymatic
  Automated blending
  Microfluidics devices
Considerations:
  Speed
  Consistency in results
  Good representation of all cell types
Arabidopsis protoplasts
Same method, different days.

## Slide 12: Factors Influencing Dissociation
Unfortunately, SC sample optimization is best achieved through trial and error…

## Slide 13: Single cell vs. nuclei
Single cell captures more transcripts, but is a harder protocol.
When to use nuclei:
  Cells cannot be harvested intact or viable (e.g. adipocytes, neurons).
  Cells are too big for capture (e.g. cardiomyocytes).
  Tissue frozen.
Tissue dissection
Cell lysis
Nuclei purification
Detergent
Grinding
Flow cytometry
Density Gradient

## Slide 14: Many protocols available…
Start here:

## Slide 15: Overview
Why single cell?
Methods – SC isolation
  Single cell isolation
  Single nuclei
Methods - sample QC
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
Cell labeling
Single cell studies at DNA Tech

## Slide 16: Factors influencing success
Cell debris / dead cells
  Clog microfluidics, free floating RNA  noise.
Aggregates
  No longer single cell data.
  Clog microfluidics.
Buffer
  Inhibit polymerase  decrease library complexity.
Storage conditions
But the most important factor is cell / nuclei counting!

## Slide 17: Workflow
Single cell suspension
Visually inspect cells
Free of debris / live
YES
Count
NO
Filter, etc.
Microscope or automated cell counter

## Slide 18: Tissue aggregates
Tissue clump
Recommended treatment: optimize tissue dissociation
DAPI stain
60X
No scale bar
Single nucleus

## Slide 19: Cell debris
Mouse DRG.
Clean DRG sample Noisy sample
Recommended treatment: filtration, centrifuge, add blocking agent.

## Slide 20: Cell debris II
Lettuce nuclei prep.
Photo credit: Mohan Prem Anand Marimuthu
Recommended treatment: modify dissociation times / detergent concentrations, change density gradient.

## Slide 21: Doublets
Non-single cell clumps.
Integrated into droplets and cannot* distinguish from single cells.
Bad for any single cell experiment.
Doublet
Recommended treatment: filtration, change [blocking agent]

## Slide 22: Dead cells (debris?)
Recommended treatment: dead cell removal.
https://www.miltenyibiotec.com/US-en/products/dead-cell-removal-kit.html

## Slide 23: Nuclei QC
Automated cell counters suboptimal, but possible with fluorescence.
  Countess II FL, Devonix CellDrop.
Stains
  Trypan blue  100% dead (not great).
  Ethidium homodimer stain (good for excluding debris).
  DAPI, PI other options
Credit: 10X
Hemocytometer
CountessII
60X: DAPI

## Slide 24: Workflow
Single cell suspension
Visually inspect cells
Free of debris / live
YES
Count
NO
Filter
Starting over >> manipulation

## Slide 25: Automated counting
Countess II.
Pros (+):
  Fast.
  Live/dead cell counts.
  Cell size estimates.
Cons (-):
  Cell size limits (4-30um).
  Doesn’t do well with odd cell shapes, debris, nuclei.

## Slide 26: Manual counting
Hemocytometer.
Pros (+):
  Reliable cell counts.
  Count small cells.
  Visualize cells vs. debris.
Cons (-):
  Slow...
http://www.wetnewf.org/pdfs/hemocytometer.html

## Slide 27: Cell sorting
Pros (+):
  Sort live / dead.
  Enrich cells of interest.
  Determine whether correct cells isolated (qPCR works too).
Cons (-):
  Overestimates cell counts (~2x).
https://flowcytometry-embl.de/cell-sorting/
FACS

## Slide 28: The good…

## Slide 29: The bad…

## Slide 30: Challenges Cell Recovery
10X is optimized for model cell types – human PBMCs, etc.
  Round, easy to count, size well below size of microfluidics.
  These yield consistent results. 10K target. 8K-10K recovered.
But most experiments outside of culture don’t look like this.
Nuclei (100% dead)
Hydra
Human bone
Variable size, shape, and viability

## Slide 31: How maximize output?
Carefully craft experimental design and sample prep .
QC cells before real sample set-up.
Concentration: aim for the median.
  700-1,200 cells per µl optimal.
  Too high  dilute.
  Too low  tough one (concentration impacts yield, pooling replicates suboptimal).
  Count in replicates (at least n=2).
Viability: 70% minimum.
  Nuclei and methanol fixed cells (0%).
Treat cells gently.
  Wide bore pipette tips, keep cells at preferred temp, work quickly..

## Slide 32: Overview
Why single cell?
Methods – SC isolation
  Single cell isolation
  Single nuclei
Methods - sample QC
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
Cell labeling
Single cell studies at DNA Tech

## Slide 33: Cell Hashing
Label cells (either oligo-tagged antibodies) or oligos.
Allows for multiplexing and super-loading scRNA-seq platforms – cost saving and minimize tech variation.
Many options available:
  MULTI-seq (C. McGinnis / Z Gartner @ UCSF)
  Biolegend TotalSeq
  BD Single-Cell Multiplexing Kit
  10X CellPlex (coming later this year)
“Cite-seq”
“MultiSeq”

## Slide 34: MultiSeq Tag Design
Oligo targeted to plasma membrane with 5’ lignoceric acid amide.
  Co-anchor increases stability and specificity.
8bp barcode conjugated to 3’ Poly-A capture sequence.
Once in droplets, PolyA mimics endogenous transcripts and hybridizes to dT oligos in beads.
“MultiSeq” (C. McGinnis)
Barcode --> tag suspension
AAAs  capture transcripts
5’
3’
AAAAAAAAAA
barcode
PCR handle

## Slide 35: Overview
Why single cell?
Methods – SC isolation
  Single cell isolation
  Single nuclei
Methods - sample QC
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
Cell labeling
Single cell studies at DNA Tech

## Slide 36
10X Single Cell Studies - DNATECH

## Slide 37
Assay summary (organism)
78 projects since July 2017 (primarily 3’ GEX).
  Sample distribution by organism
Mouse
Human
Bovine

## Slide 38: Retinal degeneration

## Slide 39: Vitamin E deficiency - DRG Neurons

## Slide 40: ‘564’ – challenges and solutions
DRG fragile, difficult to count, odd sizes (clog 10X chip?).
Count manually  better counts.
Accepted some degree of induced technical variation
  Prepped samples over three days.
  Improved sample quality and reproducibility, introduced prep day variation.
    As Matt mentioned mitigate with experimental design.

## Slide 41: Important resources
10X Genomics
  https://support.10xgenomics.com/single-cell-gene-expression
  Paul Scott, Sales Executive (paul.scott@10xgenomics.com)
UC Davis Flow Cytometry
  http://www.ucdmc.ucdavis.edu/pathology/research/research_labs/flow_cytometry/index.html
  Bridget McLaughlin (Technical Director)
UC Davis DNA Technology Core
  http://dnatech.genomecenter.ucdavis.edu/single-cell-analyses/
UC Davis Bioinformatics Core
  https://bioinformatics.ucdavis.edu/

## Slide 42: Cost 10X Reagents
Chips are single use (n=1 to n=8 samples)  $247 EACH
Reagents (n=1)  $1,350 EACH.
Total (n=1, reagents only): $1,597.
  This doesn’t include you or your cores labor!
Sequencing? Bioinformatics?
  Depends on many factors.
  We charge $1,000 for 350M reads (~10K cells with 35K reads per cell).

## Slide 43: Acknowledgements
UC Davis DNA Technology Core team.
UC Davis Bioinformatics Core team.
10X Genomics.
  Adam Bemis (Field Applications Scientist)
  Paul Scott (Sales Executive)